## Slide 1: RC CAR IOT
Rauf Pere & Darren Ofori Appiah

## Slide 2: Block Diagram
Controller
Car
Server

## Slide 3: Car System
12V battery power source
5V linear regulator for PSoC power source
MPU6050 I²C interfaced temperature sensor/
accelerometer/gyroscope
Logic level shifter using mosfets
L293D H bridge IC
Two DC motors

## Slide 4: Car System
Custom soldered circuit board for cleaner setup
Full car setup along with black 3D printed frame and battery

## Slide 5: Controller System

## Slide 6: MQTT and Security
TLS protocol (transport layer security)
CRT file: Validates client’s identity against a trusted Certificate Authority (CA)
Key file: Key of the client
PEM file: Encodes the private key of the client
Truststores are a special kind of Java KeyStores(JKS)
Enhances data integrity and prevents MITM attacks

## Slide 7: Server UI
MPU6050 data
Car orientation
Reset orientation
Motor control

## Slide 8: Power Consumption
Before and after low power

## Slide 9: Software Architecture RTOS
Controller subsystem
Read joystick x, y data
BLE communication for joystick data to car subsystem
MAX7219 array driver to showcase speed

## Slide 10: Software Architecture RTOS
Car subsystem
MQTT Client setup and regulation of MQTT connection
Speedometer calculates RPM to send via BLE to the controller subsystem
BLE communication for the controller
Motor driver PWM with joystick data